Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

May 30, 2006

West Coast Hybrids

2860 Acadia Drive

Victoria, B.C.

V9B  2C3

Dear Mr. Scott Harrison

The West Coast Hybrids L600 rocket motor was tested on April 16,2006 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/06/11 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | West Coast Hybrids | Test Date | 16/04/06 |
| --- | --- | --- | --- |
| Mfg. Designation | L600 | Samples per Second | 1000 |
| CAR Designation | L600 | Burn Time | 5.33 seconds |
| Metric Dimensions | 75 x 1016 mm | Total Impulse | 3161.28 Ns. (710.40 lb.sec) |
| Loaded Weight | 5134 gm | Maximum Thrust | 1646.59 N (370.0 lbs) |
| Burnout Weight | 2870 gm | Average Thrust | 598.75 N (134.55 lb) |
| Certified Until | 31/06/11 | Delay Times Certified | N/A |
| Propellant Weight | 2265 gr. | ISP Delivered |  |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee