Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

May  17, 2002

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro38 648 J285-15A rocket motor was tested on May 10, 2002 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 30/06/05 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 10/05/02 |
| --- | --- | --- | --- |
| Mfg. Designation |

| 648J285-15A | Samples per Second | 1000 |
| --- | --- | --- |
| CAR Designation | J285-15A | Burn Time | 2.256 seconds |
| Metric Dimensions | 38 x 367 mm | Total Impulse |

| 648Ns (145.81 lbsec) |
| --- |
| Loaded Weight | 595 gm | Maximum Thrust |

| 369.26Ns (82.98 lbs) |
| --- |
| Burnout Weight | 268 gm | Average Thrust |

| 287.51Ns (64.61 lbs) |
| --- |
| Certified Until | 30/06/05 | Delay Times Certified |

| 15,12,10,8,6 |
| --- |
| Propellant Weight | N/A | ISP Delivered | N/A |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee