Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

December 6, 2002

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 54 1195 J295-16A rocket motor was tested on 03/12/02 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/12/05 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 03/12/02 |
| --- | --- | --- | --- |
| Mfg. Designation | 1195 J295-16A | Samples per Second | 1000 |
| CAR Designation | J295 -A | Burn Time | 4.00 seconds |
| Metric Dimensions | 54x 320 mm | Total Impulse | 1196.3 Ns. (268.83 lb.sec) |
| Loaded Weight | 1119 gm | Maximum Thrust | 420.52 N (94.50 lbs) |
| Burnout Weight | 494 gm | Average Thrust | 298 N (66.96 lb) |
| Certified Until | 31/12/05 | Delay Times Certified | 16 seconds to 6 seconds, infinitely adjustable |
| Propellant Weight | 594 gr. | ISP Delivered | 205.4 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee