Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

December 29, 2002

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 54 1635 K445-17A rocket motor was tested on 03/12/02 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/12/05 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 03/12/02 |
| --- | --- | --- | --- |
| Mfg. Designation | 1635 K445-17A | Samples per Second | 1000 |
| CAR Designation | K445-A | Burn Time | 3.67 seconds |
| Metric Dimensions | 54x 404 mm | Total Impulse | 1636.3 Ns. (367.70 lb.sec) |
| Loaded Weight | 1398 gm | Maximum Thrust | 664.83 N (149.4 lbs) |
| Burnout Weight | 572 gm | Average Thrust | 445 N (100 lb) |
| Certified Until | 31/12/05 | Delay Times Certified | 17 seconds to 7 seconds, infinitely adjustable |
| Propellant Weight | 792 gr. | ISP Delivered | 210.7 |

Yours truly,

Max Baines,

Chairman											CAR Motor Certification Committee