Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

July  8, 2003

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 54 1412K530SS-16A rocket motor was tested on July 6, 2003 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/07/06 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 06/07/03 |
| --- | --- | --- | --- |
| Mfg. Designation | 1412K530SS-16 | Samples per Second | 1000 |
| CAR Designation | K530SS-A | Burn Time | 2.67 seconds |
| Metric Dimensions | 54x 404 mm | Total Impulse | 1412.0 Ns. (317.30 lb.sec) |
| Loaded Weight | 1639.8 gm | Maximum Thrust | 596.4 N (134.1 lbs) |
| Burnout Weight | 570.1 gm | Average Thrust | 529 N (118.87 lb) |
| Certified Until | 31/07/06 | Delay Times Certified | 16 seconds to 6 seconds, infinitely adjustable |
| Propellant Weight | 1025 gr. | ISP Delivered | 140.5 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee