Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

January 2, 2003

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 54 2060 K570 -17A rocket motor was tested on 03/12/02 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/12/05 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 03/12/02 |
| --- | --- | --- | --- |
| Mfg. Designation | 2060 K570-17A | Samples per Second | 1000 |
| CAR Designation | K570 -A | Burn Time | 3.59 seconds |
| Metric Dimensions | 54x 488 mm | Total Impulse | 2062.9 Ns. (463.57 lb.sec) |
| Loaded Weight | 1685 gm | Maximum Thrust | 892.67 N (200.6 lbs) |
| Burnout Weight | 652 gm | Average Thrust | 574 N (128.99 lb) |
| Certified Until | 31/12/05 | Delay Times Certified | 17 seconds to 7 seconds, infinitely adjustable |
| Propellant Weight | 990 gr. | ISP Delivered | 212.5 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee