Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

June11, 2004

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 54 2765L730-P rocket motor was tested on May 13 and May 28, 2004 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/06/07 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 13/05/04 and 28/05/04 |
| --- | --- | --- | --- |
| Mfg. Designation | 2765L730-P | Samples per Second | 1000 |
| CAR Designation | L730-P | Burn Time | 3.77 seconds |
| Metric Dimensions | 54 x 649 mm | Total Impulse | 2765 Ns. (621.35 lb.sec) |
| Loaded Weight | 2247 gm | Maximum Thrust | 1214.85 N (273 lbs) |
| Burnout Weight | 830 gm | Average Thrust | 733 N (164.72 lb) |
| Certified Until | 31/06/07 | Delay Times Certified | Plugged |
| Propellant Weight | 1351 gr. | ISP Delivered | 208.7 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee

Attachment = L730.PDF