Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

January 7, 2005

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 98 M1450-P rocket motor was tested on October 29,2004 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until January 31, 2010 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 29/10/04 |
| --- | --- | --- | --- |
| Mfg. Designation | M1450-P | Samples per Second | 1000 |
| CAR Designation | M1450-P | Burn Time | 6.87 seconds |
| CTI Case RMS Case | 98 x 702 mm 98 x 732 mm | Total Impulse | 9955 Ns. (2237.08 lb.sec) |
| Loaded Weight | 8578 gmCTI 8387 gmRMS | Maximum Thrust | 2416.35 N (543 lbs) |
| Burnout Weight | 3610gm CTI 3413gm RMS | Average Thrust | 1456 N (327.19 lb) |
| Certified Until | January 31, 2010 | Delay Times Certified | Plugged |
| Propellant Weight | 4830 gr. | ISP Delivered | 209.7 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee