Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

January 7, 2005

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 98 M520-P rocket motor was tested on June 20,2003, July 4, 2003 and October 30, 2004  and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until January 31, 2010 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | June 20, 2003, July 4, 2003 and October 30,2004 |
| --- | --- | --- | --- |
| Mfg. Designation | M520-P | Samples per Second | 1000 |
| CAR Designation | M520-P | Burn Time | 13.81 seconds |
| CTI Case RMS Case | 98 x 548 mm 98 x 579 mm | Total Impulse | 7441 Ns. (1672.13 lb.sec) |
| Loaded Weight | 6693 gmCTI 6662 gmRMS | Maximum Thrust | 1184.2 N (266.11 lbs) |
| Burnout Weight | 2871gm CTI 2812gm RMS | Average Thrust | 542N (121.8 lb) |
| Certified Until | January 31, 2010 | Delay Times Certified | Plugged |
| Propellant Weight | 3658 gr. | ISP Delivered | 204.4 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee