Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

January 7, 2005

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The Pro 98 N1100-P rocket motor was tested on  June 14, 2004 and October 30 2004, and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until January 31,2010 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | June 14, 2004 and October 30, 2004 |
| --- | --- | --- | --- |
| Mfg. Designation | N1100-P | Samples per Second | 1000 |
| CAR Designation | N1100-P | Burn Time | 12.49 seconds |
| RMS Case | 98 x 1046 mm | Total Impulse | 14005 Ns. (3147.19 lb.sec) |
| Loaded Weight | 11589gmRMS | Maximum Thrust | 2712.14N (609.47 lbs) |
| Burnout Weight | 4728gm RMS | Average Thrust | 1120 N (251.69 lb) |
| Certified Until | January31,2010 | Delay Times Certified | Plugged |
| Propellant Weight | 6790 gr. | ISP Delivered | 210.3 |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee