Canadian Association of Rocketry

CAR Motor Certification Committee

c/o 2005 - 16 St. N.

Lethbridge, Alberta

T1H 4W6

October 24, 2002

Cesaroni Technology Incorporated

2561 Stouffville Road

Gormley, Ontario

L0H 1G0

Dear Mr. Mike Dennett

The 29,990 Pro150 O5100  rocket motor was tested on 17/09/02 and is in compliance with the certification requirements and standards of the Canadian Association of Rocketry (CAR).  The motor is hereby certified until 31/12/05 for hobby rocketry use by the members of the Canadian Association of Rocketry and any other rocketry associations with current reciprocal  motor certification agreements in place with the CAR.

| Motor Manufacturer | Cesaroni Technologies. Inc | Test Date | 17/09/02 |
| --- | --- | --- | --- |
| Mfg. Designation | 29,990 O5100-P | Samples per Second | 1000 |
| CAR Designation | O5100-P | Burn Time | 5.86 seconds |
| Metric Dimensions | 160.8mm x 803 mm | Total Impulse | 29,990 Ns. (6,739.32 lb.sec) |
| Loaded Weight | 23,577 gm | Maximum Thrust | 6562 N (1474.55 lbs) |
| Burnout Weight | 10,314 gm | Average Thrust | 5113 N (1149.65 lb) |
| Certified Until | 31/12/05 | Delay Times Certified | Plugged |
| Propellant Weight | 13,245 gr. |  |  |

Yours truly,

Max Baines,

Chairman

CAR Motor Certification Committee